## Slide 1: CMOS
Oleg Ladin
27 September 2021

## Slide 2: Course materials
Lectures: https://mipt-ilab.github.io/mipt-mips/
GitHub: https://github.com/MIPT-ILab/mipt-mips/

## Slide 3: Layers of Abstraction in CS
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture
Less about electrons, semiconductors…
More about voltages, wires and transistors…

## Slide 4: Reminder: MOSFET
The metal-oxide-semiconductor field-effect transistor (MOSFET, «МОП-транзистор») acts as a voltage-controlled switch with three terminals: source, drain, and gate
There are two variations of the MOSFET: the n-channel (this slide) and the p-channel
Source
Gate
Drain
+
-
-
-
+
+
+
-
-
-
Metal
Oxide layer
P-type semiconductor
N-type semiconductor

## Slide 5: Reminder: N and P-type MOSFET
Gate | State | Input (Source) | Output (Drain)
1 | On (conduct) | 0 | 0
 |  | 1 | weak 1
0 (any other value than 1) | Off (not conduct) | any | Z
Gate
Drain
Source
Gate | State | Input (Source) | Output (Drain)
0 | On (conduct) | 0 | weak 0
 |  | 1 | 1
1 (any other value than 0) | Off (not conduct) | any | Z
Gate
Drain
Source
N-type MOSFET:
P-type MOSFET (similar to N-type, but all is inverted):

## Slide 6: Reminder: Invertor
Input | Output
0 | 1
1 | 0
Gate
Drain
Source
Gate
Drain
Source
0
Vcc
1
Input | Output
0 | Z
1 | 0
Input | Output
0 | 1
1 | Z
0
Vcc
1
Input
Output
1
0
Z
The bottom part
The top part
The full scheme
Input
Output
!A

## Slide 7: CMOS

## Slide 8: CMOS Circuits
Complementary metal–oxide–semiconductor (CMOS, «КМОП») is a technology for constructing integrated circuits
The main characteristics of CMOS devices is low static power consumption
    There is no current in static state of the scheme (i.e. the power supply is never connected to the ground)
CMOS schemes always contain two complementary parts
    One part consists of P-type transistors and is connected to the power supply and provides 1 to the output
    The other consists of N-type transistors and is connected to the ground and provides 0 to output
    When one part is turned on the other part is disabled (provides Z)

## Slide 9: CMOS NAND Circuit
A | B | Output
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
Output
0
A
B
Output
Vcc
1
A
Output
B
Vcc
1
A
Output
B
0
A
B
The bottom part
The top part
The full scheme
!(A&B)

## Slide 10: Time and Power

## Slide 11: Transistor equivalent scheme
MOSFET has some parasitic capacities...
and resistivity

## Slide 12: Timing
Capacities are not charged or discharged immediately:
Time of charge or discharge can be calculated:
It is a source of voltage delays in circuits
Vcc
Output
1
0
1
1
0
1
+ −

## Slide 13: Power Consumption in CMOS
Gate
Source
Drain
Source
Drain
0
1
Gate
Gate
Output
n
n
n
p
p
p
Input
1
+
+
-
-
0
Vcc
1
Input
Output
No current in static state, i.e. there is no power consumption
Current exists only at switch from one state to another to recharge the capacities
No connection between the power supply and the ground

## Slide 14: Recharging Power

## Slide 15: Production

## Slide 16: YouTube videos
“How a CPU is made“ explains how integrated circuits (IC) are created
“Intel: The Making of a Chip with 22nm/3D Transistors“ shows the whole process shortly
  Steps description: From sand to silicon: the making of a chip

## Slide 17: Thank You