## Slide 1: Sequential Circuits
Oleg Ladin
4 October 2021

## Slide 2: Layers of Abstraction in Computer Science (CS)
Application
Algorithms
Programming Language
Operating System
Instruction Set Architecture
Microarchitecture
Gates/Register-Transfer Level (RTL)
Circuits
Physics
Topics of
this lecture

## Slide 3: Reminder: Combinational Circuits
If the output of a function is completely defined by the current input, then the function is called combinational :
Qt = F(xt, yt, zt, …)
A lot of things can be implemented using combinational circuits
    e. g. adder, decoder, multiplexer…

## Slide 4: Sequential Circuits

## Slide 5: Sequential Circuits
If the output of a function depends not only on the current input, but on the previous state, then the function is called sequential
Main advantage - ability to remember the previous state
  Used to store information
Qt = F(xt, yt, zt, …, Qt-1)
F(xt-1, yt-1, zt-1, …, Qt-2))
F(xt-2, yt-2, zt-2, …, Qt-3)))
Qt = F(xt, yt, zt, …, Qt-1)

## Slide 6: SR Latch: Overview
S | R | Qt-1 | Qt
x | y | out
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
Q
!Q
x
y
out
y
out
≡
x
y
out
0
≡
out
Q
!Q
reset
set
0
0
1
0
1
1
0
1
NOR:
SR latch:
The simplest store element:
SR latch:
0
1
0
0
Q
Q
0
1
Q
0
1
0
Q
1
1
1
Q
0
reset
set
Q
!Q
Prohibited state

## Slide 7
reset
set
Q
!Q
R
!Q
S
Q
S | R | Qt-1 | Qt
0 | 0 | Q | Q
0 | 1 | Q | 0
1 | 0 | Q | 1
1 | 1 | Q | 0
S
0
1
R
0
1
Q
0
1
!Q
0
1
?
?
But, which signal will be really faster will depend on many factors (e.g., temperature).
The output will be determined by the fastest signal
SR Latch: Timing

## Slide 8: D Latch
Don’t have prohibited states
Asserted by a level of the write enable signal (we)
Store one bit of information
Can be used as building block for creating static memory arrays
S
Q
R
!Q
Write enable
Data
D
we
Q
D | we | Qt-1 | Qt
D | 0 | Q | Q
0 | 1 | Q | 0
1 | 1 | Q | 1

## Slide 9: Edge-triggered D Latch (D flip-flop)
Don’t open for writing neither at we =0 nor at we =1
It is open for a very small amount of time when the write enable goes from 0 to 1
  It is a trigger asserted by the positive edge of write enable signal
Such types of triggers are mostly used to organize pipelined execution
There are several common flip-flop / latch types:
  SR (“set-reset”), D (“data” / “delay”), T (“toggle”), JK
D | we | Qt-1 | Qt
D
Q
clk (we)
D
0
Q
Q
D
1
Q
Q
D
↑
Q
D
D
↓
Q
Q

## Slide 10: Single port 2MxN Memory Array
Memory array has 3 input signals and 1 output
Data buses are N bits wide (each chunk is N bits)
Address is M bits wide if 2M is array size
Memory
Array
address
input data
output data
M
N
N
Write enable
Memory
Array
address
input data
output data
2
1
1
Write enable

## Slide 11: Critical paths

## Slide 12: What is a critical path of scheme?
Critical path is the slowest logic path in the circuit
Reliable result of whole logic path can not be ready until critical path is passed by signal

## Slide 13: Example of critical path finding: Multiplexer
1t
1t
1t
2t
= 5t

## Slide 14: Next time – practice
More examples of combinational and sequential circuits
You will need the Logisim app:
  Install Java: https://www.java.com/ru/download/
  Download Ligisim: https://sourceforge.net/projects/circuit/

## Slide 15: Thank You