## Slide 1: Caches: part 3
Daniil Vorobyev
21.02.2022

## Slide 2: Agenda
Memory Wall
Spatial and temporal locality
Hardware implementations
Performance metrics
Software optimizations
Hardware optimizations (prefetching & replacement)
Write handling
Multi-level cache organization

## Slide 3: Refresher
Main memory is large, but slow
Solution: memory hierarchy with caches
  utilizes temporal and spatial locality of workloads
  provides visibility that memory is usually fast
Bad scenario: cache misses
  Compulsory
  Capacity
  Conflict
L1
L2
L3
Cache
CPU
Main Memory
smallest, but fastest
slowest, but largest

## Slide 4: Prefetching

## Slide 5: Prefetching: main idea
Prefetching – predict future memory accesses
  A useful prefetch eliminates a potential cache miss
2 types of prefetching:
  Software Prefetching: special prefetching instructions
  Hardware Prefetching
Code prefetching is performed by a branch predictor
Prefetch Limitations
  Prefetching relies on extra memory bandwidth
  Too aggressive/inaccurate prefetching slows down demand fetches

## Slide 6: Quality metrics
Accuracy
  Portion of prefetched lines which eventually become demand-hits
Coverage
  Portion of cache misses removed by prefetching
Timeliness
  Reduction of cache miss time
For L1 cache prefetch schemes with high accuracy are used
Bigger caches usually leverage schemes with higher coverage

## Slide 7: Next sequential
On a cache miss, prefetch sequential cache line (± 64 bytes)
Prefetch metrics:
  Moderate accuracy
  Low coverage
  Lack of timeliness (prefetch performed too late)
Simple HW
Works well for instructions prefetch
“Fallback" if more complex methods not available
  lw $t0, 0x0($t1)
prefetch 0x40($t1)

## Slide 8: Stride detection
HW detects the repetitive step of a load and prefetch data in advance
Prefetch metrics:
  High accuracy (for long loops)
  Low coverage
  Highly timeliness
Issues with unrolled loops
  Initially single load operation occupies multiple entries in detector
  0x00402f0: lw $t0, 0x20($t1)
  0x00402f4: add $t2, $t2, $t0
  0x00402f8: addi $t1, $t1, 0x100
  0x00402fc: beq $t1, $t3, -4
IP | Stride | Last address
0x00402f0 | 0x100 | 0x00f4180
prefetch 0x00f4280
prefetch 0x00f4380
...
Detector

## Slide 9: Stream detection (1)
HW detects stream with the repetitive step
  Similar to the previous technique, but without reference to IP
Example:
0xba20200
0x3cf1140 0xba203с0
0x3cf1100
0x3cf10c0
0x3cf1080
0xba20740
0xba20900
...
prefetch 0xba20ac0
prefetch 0x3cf1040
...
Base address | Stride | Last address
0xba20200 | +0x1c0 | 0xba20900
0x3cf1140 | −0x40 | 0x3cf1080
0xba20200
0x3cf1140 0xba203с0
0x3cf1100
0x3cf10c0
0x3cf1080
0xba20740
0xba20900
...

## Slide 10: Stream detection (2)
Stream detection without repetitive step
  load pattern not found, only direction – load everything following this direction
Prefetch metrics:
  Low accuracy
  High coverage
  Highly timeliness
0xba20200 0xba20340
0xba203a0
0xba204с0
0xba20520
...
prefetch 0xba20560
prefetch 0xba205a0
...
Base address | Stride | Last address
0xba20200 | +???? | 

## Slide 11: Replacement

## Slide 12: Cache Line Replacement
When miss occurs need to free space in a cache for a new line
Direct mapped cache
  A new line is mapped to a single entry → evict old line from the entry
N-way set associative cache
  Choose a victim from all ways in the appropriate set, but how?
FIFO (First In First Out) replacement
  Easy to implement in HW, but can violate temporal locality
LRU (Least Recently Used) replacement
  Evict the most unused line (was not accessed longer than other)
  Good temporal locality, but complex HW → use simplified pseudo-LRU

## Slide 13: Pseudo-LRU
Pseudo-LRU is a good approximation of LRU with a binary tree
Each node stores information about which of the descendants was recently used
L
R
L
A
B
C
D
R
L
L
A
B
C
D
Request «B»
L
R
R
A
B
E
D
R
R
L
A
B
C
D
Request «A»
Request «E»

## Slide 14: Counterexample
Sometimes there is no temporal locality
  Example: read of large data array (data size >> cache size)
In case of LRU the second loop will always ‘miss’
If data eviction follows MRU policy (most-recently used) the second loop will start with ‘hit’
  for (size_t i = 0; i < N; ++i)
  sum += a[i];
  double average = sum / N; for (size_t i = 0; i < N; ++i)
  a[i] -= average;

## Slide 15: Write handling

## Slide 16: Cache write policies
Memory writes (store instructions) also need to update a cache
WriteThrough: always update both memory and cache
  + Coherence: cache and memory are always in the same state
  - Higher utilization of memory bandwidth
WriteBack: update only cache, update memory at line eviction
  + Low store latency and memory bandwidth
  - Risk of data loss, requires snoops – coherency checks

## Slide 17: Multi-level cache organization

## Slide 18: Motivation for multi-level caches
Only L1 cache: a large miss penalty due to memory access
With L2 cache: L1 miss penalty is reduced
  Now, on L1 miss we access L2, not memory
L2 Cache is larger (lower MissRate), but has higher latency
Example:
L2
<T> ≈ T_L1hit + MissRateL1 * T_mem
<T> ≈ T_L1hit + MissRateL1 * (T_L2hit + MissRateL2 * T_mem)
<T> ≈ 3 + 0.08 * 200 = 19 clk
<T> ≈ 3 + 0.08 * (6 + 0.03 * 200) = 3.96 clk
x5 !
L1
CPU
Main Memory

## Slide 19: Multi-level inclusion policies
1. Inclusive
2. Exclusive
3. Non-Inclusive/Non-Exclusive (NINE)
L2
L1
L2
L1
modified only
modified only
M/NM
modified only
+ low bandwidth
- lines duplications
+ effective cache usage
- higher bandwidth
L2
L1
combination of 2 policies
M/NM
modified only