## Slide 1: TLP. SMT
Danila Khaidukov
11.04.2022

## Slide 2: Motivation
Superscalar is hard to scale:
  ILP is depleted – all independent instruction are already executed in parallel
  Inefficient – power & area grows faster than performance
Alternative way to use area is Multicore:
  1 big core - 6x area with 3x performance
  3 small cores (2x area & performance each) - 6x area with 6x performance boost in total
  2x efficiency!

## Slide 3: Thread-level parallelism
Running tasks can be separated into independent execution threads
  multiple applications running simultaneously
  from a single application – parallelized by a programmer
Single-core CPU utilizes instruction-level parallelism (ILP) of 1 thread
Multicore utilizes thread-level parallelism (TLP)
  Each thread is executed on single core

## Slide 4: Types of multiprocessors
All processors works with one address space
SMP — Symmetric Multi Processing
  Identical processing units with a single shared memory
  Fast and effective memory usage
  Low scalability due to lots of interconnections and limited memory throughput
NUMA — Non Uniform Memory Access
  Each processing unit with its own memory and shared memory bus
  Highly scalable
  Requires special coherency protocols and OS support

## Slide 5: Multiprocessor vs Multicore
Multiprocessor: sharing memory on CPU level
  Original approach
  Good for independent workloads
  Bad for cooperative workloads with data exchange
Multicore: sharing memory between cores of 1 CPU
  More advanced approach on a single chip
  Shared cache and memory bus
  Data exchange through the shared cache
CPU 1
CPU 2
Memory
CPU
core 1
core 2
Cache
Memory

## Slide 6: Memory Coherence in a multicore system
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
Each core has its own local cache
  Cores can keep multiple local copies of the same data
  Multiplied data can be damaged if one core modifies it:
[X] ≡ 10
[X] ≡ 20
20
Memory: Mem[X] ≡ 10
Core 0: a = Mem[X] # a = 10
Core 1: Mem[X] = 20
Core 0: b = Mem[X] # b = 10
miss
miss
[X] ≡ 10
hit
Error: read the old value from the local cache
[X] ≡ 10
20
Memory must be coherent:
  All cores must see memory identically
  All cores must see the latest state of memory

## Slide 7: Coherence protocols: MESI
 | Valid? | Owned? | Modified?
Invalid | NO | NA | NA
Shared | YES | NO | NO
Exclusive | YES | YES | NO
Modified | YES | YES | YES
Coherence protocols describe how to handle writes/reads to maintain memory coherence in a multicore system
Example: MESI protocol
  Define 4 states of a cache line
  Describe transactions between states
State rules:
  To modify a line, ownership should be obtained first
  There is no state when a line is modified and contained by other cores

## Slide 8: MESI: example
Local
Cache
Core 1
Local
Cache
Core 0
Main Memory
Shared Cache
[X] ≡ 25
[X] ≡ 35
[X] ≡ 25
[X] ≡ 25
Memory: Mem[X] ≡ 25
Core 0: a = Mem[X] # a = 25
Core 0: Mem[X] ≡ 35
Core 1: b = Mem[X] # b = 35
  Snoop [X]
    Core 0 writeback [X]
Core 1: Mem[X] ≡ 45
  Request ownership for [X]
    Core 0 invalidate [X]
35
[X] ≡ 25
(1, 0)
E
M
35
35
[X]
(1, 1)
S
S
[X]
I
(0, 1)
[X]
M
45

## Slide 9: MESI State Diagram
read shared
read not shared
read
read
read
write
write
write
write
read
write
snoop
request ownership
snoop
snoop
snoop
snoop
request ownership
request ownership
request ownership
request ownership
Shared
Modified
Exclusive
Invalid

## Slide 10: SMT

## Slide 11: Motivation
Core must be universal at fixed superscalar width
  Extract as much ILP as possible
  Effective usage of hardware
Threads could interact through shared memory
  Coherence protocol limits performance
Previously each thread was executed on separate single core
  Now assume each core could handle more than one thread execution
  CPU supports ST and MT execution modes
3
1
2
0
2nd application
1
2
3
1st application
0

## Slide 12: Simultaneous Multithreading
Physically we have the same amount of cores
Logically there are twice more cores
  OS schedules tasks on logical CPUs
Each logical processor maintains its own arch state
  Complete set of architectural registers (General-purpose registers, Control registers, Machine state registers, Debug registers)
  Instruction pointers
Each logical processor has its own interrupt controller
CPU
Core 1
Core 2
Cache
Memory

## Slide 13: Resource Sharing
Each pipe-stage is occupied by one of the threads
Resources are either replicated, partitioned or shared
Replicated resources are ones which are vital to maintain two fully independent contexts on each logical processor
  Main source of HW size growth
Partitioned resources are mostly queues that decouple pipeline stages
  Could be unified in ST execution mode
Shared resources are ones which don’t care about threading at all
Arch State
Physical Registers
Arch State
APIC
Fetch
Decode
Queue
Queue
Rename & Allocate
OOO Scheduler / Execute
ROB
ROB
Retirement
Queue
Queue
PC
PC
APIC
SQ

## Slide 14: Example: Branch Predictor sharing
BP operates in terms of virtual addresses and has shared structure in MT mode
To avoid potential aliasing problems in case of virtual address overlapping BP entries could be marked with thread ID

## Slide 15: Example: Schedule queue sharing
In MT mode schedule queue is dynamically partitioned
Each thread has its own small number of SQ entries
  This prevents one thread monopolize whole machine resources
  Each thread has ability for forward execution
Remained entries could be allocated by any thread
Schedule queue entries

## Slide 16: Example: ROB replication
In MT mode ROB is partitioned, each part contains instructions only from one thread
  Provide fairness execution of each thread
  It’s complicated to make sharing scheme with dynamic repartitioning
Each thread has its own retirement logic
  Stall in one thread doesn’t block retirement of another thread
In case of mispredictions, only instructions from affected thread are cleared
Retirement point (thread 1)
Retirement point (thread 2)

## Slide 17: Example: Data cache sharing
Caches are addressed in physical addresses and considered as shared
  If the data is common (cooperative workload), both threads hit to cache
  Otherwise, LRU algorithm works
  Ambiguity is avoided: physical address is thread-independent

## Slide 18: Resource sharing: pipeline overview
Overhead on HW size mostly comes from replicated resources
  2x ARF, 2x PC, 2x APIC
  Additional HW for thread switching between pipeline stages (thread selectors)
Still overhead is much less than 2x core

## Slide 19: SMT pros and cons
Pros:
  Increases overall system’s throughput by utilizing machine resources more effectively
  Shadow pipeline hazards and allocation stalls
  Introduce little addition HW (only replicated resources)
Cons:
  ST performance of each thread is smaller
  Could significantly drop performance due to cache thrashing
  Unlikely help traces with enough ILP or high memory bandwidth

## Slide 20: Implementations
SMT technology been around 1950s
  First researched by IBM in ACS-360 project (1968)
  Dean M. Tullsen et al – Simultaneous Multithreading: Maximizing On-Chip Parallelism – University of Washington (1995)
  Major commercial CPU – DEC Alpha 21464 w/ SMT4 (cancelled 2001)
  Intel Pentium 4 / Xeon – SMT2 support in NetBurst architecture (2002)
Modern implementations:
  2 threads: Intel Atom/Core i7/Xeon (since 2008), AMD Ryzen, IBM Power 6
  4 threads: Intel Xeon Phi, IBM Power 7 (8 cores - 32 threads)
  8 threads: IBM Power 8/9 (12 cores – 96 threads)

## Slide 21: Synchronization

## Slide 22: Synchronization
We have already discussed Memory Coherence
  Single core: Cache write policies (WriteThrough and WriteBack)
  Multicore: MESI protocol
These mechanisms guarantee data correctness, while not algorithm correctness
  Due to data races in Concurrent computing
Parallel cooperative tasks with common data require synchronization mechanisms:
  Atomic operations
  Transactional memory

## Slide 23: Atomic operations
Synchronization with atomic operations
  Ability to read and modify memory atomically (read-modify-write)
  E. g. semaphores, MutEx (mutual exclusion), shared memory
Implemented as extensions of ISA (RISC-V):
  Atomic memory operation (AMO) instructions (R-type) – for simple operations:
    AMOSWAP.W; AMOADD.W; AMOMAX.W …
  Complex Lock-free atomic read-modify-write operation: Load Reserved (Load Linked) + Store Conditional
try:
lr.w t0, (a0) # load value
# <update t0>
sc.w t1, t0, (a0) # try to update
bnez t1, try # retry if SC failed
SC returns 1 to T1 only if (A0) was not changed after LR of (A0)

## Slide 24: Transactional memory
Transactional memory – allows a group of loads and stores to execute in an atomic way
Basically, the extension of LR/SC for a memory region
Helps workloads with little conflicts among threads:
  Provides Optimistic concurrency control (OCC) – allows threads run in parallel without acquiring locks, assuming the intersection will not occur
  Transaction is committed if conflict is not present. Otherwise it is reverted to initial state and rerun until conflicts are resolved.
  Avoids deadlocks, while livelocks are still possible

## Slide 25: Thank You